Diode WaveShaper : 100-1002 Revision: A

Bill Of Materials October 20, 2002, Rev. 002

Deletes components for unused stages.

Adds recommended jacks, pots, knobs, switch, missed parts such as ferrite bead.

This BOM assumes that headers will not be used, instead wires are soldered straight to the board.

Item	Quant	Reference					Mouser Part Number

______________________________________________

1 	2 	C2,C1 10uF 					140-XRL25V10

2 	22 	C3,C4,C5,C6,C7,C8,C9,C10, .1uF 	80-C410C104M5U

C11,C12,C13,C14,C15,C16,

C17,C18,C19,C20,C21,C22,

C23,C24

3 	14 	D1,D2,D3,D4,  1N914 	78-1N914

D9,D10,D11,D12, D17,D18,D19,D20,

D22,D23

4 	1 	D21 1N751 					610-1N751A

5

6 	7 	2 	Q1,Q2 2N3904 				625-2N3904

8 	2 	Q4,Q3 2N3906 				625-2N3906

9 	32 	R1,R10,R12,R15,R16,R17, 100K 		271-100K

R18,R19,R20,R21,R22,R23,

R24,R25,R26,

R39,R40,R41,

R42,R43,R44,R45,R46,R47,

R48,R49,R50, R70,R74,R75,

R78,R79,

10 	5 	R2,R3, R7,R9,R11, 49.9K 	271-49.9K

11 	2 	R5,R73 200K 				271-200K

12 	3 	R8,R64,R72,R101,R102,R103,R104 1K 	271-1K

13 	2 	R63,R68 10K 				271-10K

14 	1 	R65 20K 					72-T20YP-20K

15 	2 	R71,R66 10 					271-10

16 	1 	R67 30K 					271-30K

17 	1 	R69 24.9K 					271-24.9K

18 	1 	U1 TL071 					511-TL071CN

19 	6 	U2,U3,U4, U7,U8, TL072 	511-TL072CN

U11

20 	1 	U12 LM336 					511-LM336Z

21	7	Jack, ¼” mono 112A			502-112A

22	4	Jack, ¼” stereo switched 114B		502-114B

23	5	Pot, 10K Linear				594-249-7103

24	5	Pot, 100K Linear				594-249-7104

25	1	Switch, SPST				633-M201202

Don’t forget these other parts

Stooge Panel, 3U

Long Stooge PCB bracket

Jim Patchell PCB

MOTM standard power cable

Wire, 22 ga stranded

Solder